## Slide 1
Design of Micro/Nano Sensors Report
Piezoresistive Sensor Based on High Performance Flexible Pressure Sensitive Film Material
11911736 冯硕
11910603张睿贤
11911007周宇轩
11910609张弼弘

## Slide 2
Introduction
OUTLINE
Traditional mechanical pressure sensors are
(a) rigid materials such as metal conductors or semiconductors
(b) the flexible pressure sensor made of polymer piezoelectric material and conductive polymer composite materials

## Slide 3
目录
CATALOGUE
Background and Current Research Results
Theoretical analysis and material
Simulation: Mirostructure Comparation
The Prosperities and Applications

## Slide 4
1
Background and Current
Research Results

## Slide 5
Classification of Flexible
Pressure Sensors
Three common transduction mechanisms
piezoresistivity
capacitance
piezoelectricity
Schematic illustration of three common transduction mechanisms and representative devices:(a) piezoresistivity; (b) capacitance; and (c) piezoelectricity.

## Slide 6
Current Research Results
Material/structure type I
Conductive Polymer Composites
elastic composite material with a pressure-sensitive effect formed by uniformly dispersing the conductive particles in the insulating polymer composites
炭黑、碳纳米管、石墨烯等分散在硅胶(PDMS)、环氧树脂

## Slide 7
Sensitive Layer Surface Micro-structure
periodic surface micro-structures, the contact resistance, generated between electrodes or micro-structures, is also a way to prepare excellent flexible piezoresistance sensors.
PDMS materials have excellent elasticity, chemical stability, biophase and plasticity.
OFET (Organic field-effect transistor)
Current Research Results
Material/structure type II
the schematic representation of an OFET-type flexible pressure sensor made from a PDMS film with an inverted pyramid-type microstructure.

## Slide 8
Sponge Foam Structure and Carbon Skeleton
MAKE polymer material into sponge foam structure or carbon skeleton has become an important sensitive material of new flexible piezoresistive sensor
Melamine
(a) Schematic diagram of carbonization of melamine sponge and preparation of flexible pressure sensors; (b) Schematic diagram of carbonized melamine sponge packed in PDMS matrix to make friction generator and adsorbed CNT to make flexible pressure sensor
Current Research Results
Material/structure type III

## Slide 9
Current Research Results
Material/structure type IV
Electrical-Conductive Fabric and Paper
Inspired by flexible pressure sensors as wearable sensors, conductive fabric and conductive paper have also become a choice of new sensor-sensitive materials.
Gold nanowires/cotton paper fiber sensor in pulse measurement and non-contact sound measurement

## Slide 10
2
Theoretical analysis and material

## Slide 11
The structure of surface microstructure
Two important property
Hemispherical microstructure
CNT/PDMS
Preparation method, surface morphology and sensitive mechanism

## Slide 12
two-sided, single-sided
and no microstructures
Pressure
The finite element analysis shows that the deformation of the sensitive membrane is basically concentrated on the microstructure under the pressure of 60.5kpa
Gold nanowires/cotton paper fiber sensor in pulse measurement and non-contact sound measurement

## Slide 13
Selection of the preparation process
Screen printing process
  Better pattern accuracy and film thickness
Electrospinning method
high-performance sizing agent and good
pattern accuracy and film thickness

## Slide 14
Selection of the conductive filler
Carbon nanotubes
Easy to entangle and agglomeration, but not easy to disperse
Graphene
Excellent electrical conductivity and mechanical properties.
the conductive material is also prone to crimp and agglomeration in the polymer matrix material
carbon black
High conductivity, easy dispersion and low cost

## Slide 15
3
Simulation: Mirostructure Comparation

## Slide 16
Preparation
Three Mirostructure: 10um*10um, the same intervel
Single pyramid
Double pyramid
Double sphere
Materials: PDMS
Parametric scan F(load): 0~1000Pa (low pressure)

## Slide 17
Calculation

## Slide 18
Calculation

## Slide 19
Data post-processing
? ? ?
结构+网格？
材料设置？
计算方式？

## Slide 20
4
The Prosperities and Applications

## Slide 21
Vibration Detect in the Environment
The equipment performance detect system
  Detect equipment vibration states
The smart home system
  Detect electronics vibration.
  Vibration trigger action

## Slide 22
Vibration Detect in the Wearable Device
Heartbeat Detect
  Pulse detect
Voice Detect
  Distinguish words
  Artificial throat

## Slide 23
Electronic Skin
Force detect
  Touch perception
  Clamp force detect
  Deformation detect
Temperature detect
  Detect electronics vibration

## Slide 24
Thanks for your patients!